## Slide 1: ARM Microcontroller: System Overview
Prof. Yasser Mostafa Kadah – www.k-space.org

## Slide 2: Recommended Reference
STM32F100xx Advanced ARM-Based 32-Bit MCUs, RM0041 Reference Manual, ST Microelectronics (Available Online)

## Slide 3: Lecture Contents
Course Goals
Course Prerequisites
Microprocessor and Microcontroller
Microcontroller Architecture
STM32 ARM Platform
Value Line Discovery Development Kit
ARM Demo Project
Assignments

## Slide 4: Course Goals
At the end of this course, you should be able to:
  Understand the architecture of one of the most popular microcontroller (MCU) families
  Use an integrated development environment (IDE) to program and debug an MCU
  Program an MCU using C language
  Understand and use peripherals integrated into an MCU
  Interface an MCU to simple external components
  Use example timers in various modes
  Understand and use interrupts
  Understand and use analog to digital converters (ADC) and digital to analog converters (DAC)

## Slide 5: Course Prerequisites
A course in Electric Circuits that includes understanding basic electronic components such as resistors, capacitors, diodes and transistors
A course in basic digital logic design that includes logic gates and Boolean arithmetic
Ability to program in a high-level programming language such as C or C++

## Slide 6: Microprocessors and Microcontrollers
Microprocessor: general-purpose CPU
  Emphasis is on flexibility and performance
  Generic user-interface such as keyboard, mouse, etc.
  Used in a PC, PDA, cell phone, etc.
Microcontroller: microprocessor + memory on a single chip
  Emphasis is on size and cost reduction
  The user interface is tailored to the application, such as the buttons on a TV remote control
  Used in a digital watch, TV remote control, car and many common day-to-day appliances

## Slide 7: Microcontroller Architectures
Microcontroller architecture refers to the internal hardware organization of a microcontroller
Each hardware architecture has its own set of software instructions called assembly language that allows programming of the microcontroller
Some of the popular microcontroller architectures
  Intel 8051
  Zilog Z80
  Atmel AVR
  Microchip PIC
  ARM

## Slide 8: Harvard and von Neumann Architectures
Harvard Architecture—a type of computer architecture where the instructions (program code) and data are stored in separate memory spaces
  Example: Intel 8051 architecture
von Neumann Architecture—another type of computer architecture where the instructions and data are stored in the same memory space
  Example: ARM and Intel x86 architecture (PC processors)
Notes: Basic difference between two of the most common types of architectures.

## Slide 9: ARM Processors
ARM: Advanced RISC Machines
  Previously “Acorn RISC Machines”
  ARM1: 1985
  Now: ARM11, ARM Cortex A, ARM Cortex R, ARM Cortex M

## Slide 10: STM32 Platform

## Slide 11: STM32 Product Lines

## Slide 12: STM32 Value Line Block Diagram

## Slide 13: STM32 Value Line Devices

## Slide 14: STM32 Value line Discovery Kit
The cheapest and quickest way to discover the STM32 Value line family
Embedded ST‑LINK or ST‑LINK/V2 included to debug applications
Works with several popular IDEs
  MDK-ARM (Keil)
  EWARM (IAR)

## Slide 15: Kit Features
STM32F100RBT6B microcontroller, 128 KB Flash, 8 KB RAM in 64-pin LQFP
On-board ST-Link (for programming and debugging)
Two red LEDs; LD1 for USB communication, LD2 for 3.3 volts power on
Designed to be powered by USB or an external supply of 5 V or 3.3 V
Can supply target application with 5 volts and 3 volts
Two user LEDs, LD3 and LD4 (green and blue)
Two push buttons (User and Reset)
Extension header for all QFP64 I/Os for quick connection to prototyping board or easy probing

## Slide 16: Kit Hardware Block Diagram

## Slide 17: Demo Project

## Slide 18: Assignments
Explain the differences between MIPS and DMIPS.
Compare the major ARM processor families available today from the points of view of processing power, cost, applications. (Hint: focus on ARM11 and ARM Cortex series processors)
Install the MDK-ARM Evaluation Version and compile and link the kit’s demo software available from ST web site.
Revision of C programming.