## Slide 1: Computer Aided Diagnosis: Feature Selection
Prof. Yasser Mostafa Kadah – www.k-space.org

## Slide 2: Recommended Reference
Recent Advances in Breast Imaging, Mammography, and Computer-Aided Diagnosis of Breast Cancer, Editors: Jasjit S. Suri and Rangaraj M. Rangayyan, SPIE Press, 2006.

## Slide 3: CAD

## Slide 4: Feature Extraction and Selection
Feature extraction and selection in pattern recognition are based on finding mathematical methods for reducing dimensionality of pattern representation
A lower-dimensional representation based on independent pattern descriptors is important
  Plays crucial role in determining separating properties of pattern classes
The choice of features, attributes, or measurements to be included has an important influence on:
  Accuracy of classification
  Time needed for classification
  Number of examples needed for learning
  Cost of performing classification

## Slide 5: Feature Selection
Features extracted from images need not represent significant information to diagnosis
  May describe aspects of no relevance to the pathology of interest
  May vary a lot with acquisition settings (pose, processing, etc.)
Several problems should be mitigated in feature selection
  Features that do not correlate with pathology
  Features that are not independent
Building classifiers with features not properly selected will:
  Cause problems in the training phase
  Will not yield the best overall classification accuracy

## Slide 6: Statistical Significance of Features
Idea: if the feature changes consistently with pathology, then the hypothesis of a statistically significant difference between the set of values for normal and abnormal cases will be true
  Inferential Statistical tests like Student t-test should detect a difference

## Slide 7: Statistical Significance of Features
Student t-test steps:
  Consider a particular feature of interest
  Divide the values into two sets for normal and abnormal cases
  Compute the mean and standard deviation for both sets
  Use the t-test to compute the p-value of the null hypothesis that both sets do not have a statistically significant difference
  The feature is suitable if the p-value is small (e.g., 0.05, 0.01, etc.)

## Slide 8: Statistical Significance of Features
Important to keep in mind that large difference in value does not mean statistical significance
  Data dispersion is a key factor
General form: multiple groups
  Diagnosis not detection
  More general inferential statistics
Nonparametric methods
  Kolmogorov-Smirnov test
  Wilcoxon signed rank test

## Slide 9: Assessment of Feature Independence
Some features may end up being dependent
  Example: feature computed as a constant factor of another
  Only one of them should be included in the input to classification stage
Several methods can help identify such dependence
  Pearson’s linear correlation coefficient
  Principal component analysis

## Slide 10: Pearson’s linear correlation coefficient
Computes the correlation between a given pair of features
Computing formula:
The value of r lies between -1 and 1, inclusive
  Value of 1 is called “complete positive correlation”: straight line y = c x
  Value of -1 is called “complete negative correlation”: straight line y= -c x
  Value of r near zero indicates that the variables x and y are uncorrelated

## Slide 11: Principal Component Analysis
Computes the eigenvalue decomposition of the matrix of features
  Rank of matrix = number of independent features
  Directions of principal components may have different performance in classification

## Slide 12: Retrospective Assessment of Features
Retrospective: evaluation after seeing the classification results based on these features
Basic idea: use for classification and then choose the features that produce the best results
  Exhaustive search
  Branch and Bound Algorithm
  Max-Min Feature Selection
  Sequential Forward and Sequential Backward Selection
  Fisher's Linear Discriminant

## Slide 13: Exhaustive Search
Let y with y = [y1,y2, … , yD] be a pattern vector, exhaustive search selects the d best features out of the maximal available features D as to minimize the classification error
The resulting number of total combinations is:
Main advantage: guaranteed best answer
Main disadvantage of exhaustive search is that the total number of combinations increases exponentially with the dimension of the feature vector

## Slide 14: Branch and Bound Algorithm
Solves the problem of huge computational cost associated with the exhaustive search
New technique to determine the optimal feature set without explicit evaluation of all possible combinations of d features
This technique is applicable when the separability criterion is monotonic:
Combinatorial optimization
Efficient computation

## Slide 15: Assignments
Apply 2 feature selection methods to the features obtained from previous tasks and compare their results
Add a random data vector as a feature to your extracted features and report how your feature selection strategy was able to detect that it is irrelevant
Add a new feature as the sum of two existing features to your extracted features and report how your feature selection strategy was able to detect that this new feature is dependent